## Slide 1: Manufacturing Technology Survey / Assessment Sheet Tutorial

## Slide 2
■Overview
Manufacturing Technology Survey Sheet is a tool to identify a new point from the experienced parts, technology, and process in order to pick out manufacturing quality risk or product reliability risk at an early stage for part approval of new semiconductor device with new technology/process.
It is designed to be used as a communication tool for semiconductor makers, ECU makers, and Car makers. Comparison with the experienced semiconductor products, technology, and process is performed based on the following content.
・Select a new product and an experienced product (multiple selection available) for comparison
・Clarify the differences between new products and experienced products
in terms of the manufacturing methods and materials of each technical aspect
・Check the level of technological new point based on the differences between each technical aspect,
and narrow down the items that need to be considered
・Extract 4M1E impacts and concerns on items requiring consideration
Manufacturing Technology Assessment Sheet is a tool to identify the evaluation level and qualification items for new points in the manufacturing process and is intended to be used as a communication tool for semiconductor makers, ECU makers, and Car makers. Based on the following content, it clarifies the scope of qualification required for new part approval and the products to be tested.
・Add new points in 4M1E and associate these points with the evaluation items.
・Add a design checklist for part approval to clarify the impact of new adoption on electrical equipment and systems
・Link evaluation items including combination aspects, actual result, failure mechanisms, and representative product
■Purpose
・Optimization of evaluation item selection by identifying failure risk concerning new manufacturing process
・Throughput improvement and man-hour reduction at suppliers by using a common form
・Assurance of quality and reliability and time reduction in evaluations for approval of newly developed part
Restricted
Purpose of Manufacturing Technology Survey / Assessment Sheet

## Slide 3
■Sheet structure
Section a) Overview of new product and comparison product:
Appropriately select reference product(s) whose technology is used in the new product and enter the product description, product name, and overview of each part (main specifications, manufacturing site, quality grade, performance, etc.)
Section b) New and changed points of each technical aspect in each process:
The "Technical Elements" section lists typical items that have been discussed as confirmation items in the past by semiconductor makers and ECU makers when adopting new products (some items are not included in the confirmation items in Appendix 2:CDCQ of AEC-Q100 Rev.H).
Since the purpose of this sheet is to identify new products and new technologies, any completely new technical aspects or process methods not listed on the sheet must be entered by adding rows.
・Filter by package type to show the items you need to fill in
・Refer to the "Description" column and fill in the details of the new product. Similarly, fill in the details of the reference product(s).
Restricted
Structure of Manufacturing Technology
Survey Sheet
Section a)
Section b)
Section c)
Section d)
Section e)

## Slide 4
■Sheet structure
Section c) Impact of combination with new technology and its content:
Enter "Yes" in the "Combination with new technology” section if any combination of technological aspects is newly used. Fill in the description of the new technological aspect(s) in “Affected combination”.
Section d) Technical level:
In the "Technology level" field, if the technology of the new product is the same as that of the reference product(s), select “Existing," if it is similar, select “Minor Change" and if it is different, select “New Technology“. If “New Technology“ or “Minor Change" is selected, enter the difference between new and existing product(s) (including the technology combination with related processes and materials) and the reason if it is not applicable.
Section e) Impacts and concerns of 4M1E:
For “New Technology“ or “Minor Change“ item(s), specify the change point(s) from the existing product(s) in terms of 4M1E and fill in its concerned risk. The new points/changes extracted on this sheet are then entered into evaluation items on Manufacturing Technology Assessment Sheet.
*Table 1 on the next page shows the criteria for determining whether it is “Existing” / “Minor Change” / “New Technology” compared to the existing product(s) for automobile in terms of 4M1E.
Restricted
Structure of Manufacturing Technology
Survey Sheet
Section a)
Section b)
Section c)
Section d)
Section e)

## Slide 5
■Table 1－Judgement index proposal by 4M1E change point from experienced product
Restricted
Structure of Manufacturing Technology
Survey Sheet

## Slide 6
Section a)
Overview of new product and comparison product:
a-1) Fill in “Product Description”, “Manufacturing Site”, and “Quality Grade, Performance” information of the subject new product
a-2) Fill in “Product Description”, “Manufacturing Site”, and “Quality Grade, Performance” information of the reference product(s). In addition to single products, processes and product series as experienced technical aspects can be also acceptable as reference (Add columns as necessary)
a-3) If the actual production volume for a single product is too small, the one for multiple products in the same process (production start time and cumulative production volume) are also acceptable.
a-2
a-3
a-1
Restricted

## Slide 7
Section b)
New and changed points of each technical aspects in each process:
b-1
b-2
b-3
b-4
Restricted
b-1) To clarify the target technical aspects, enter “X” in the technical aspects of the target package. At that time, the multi-chip (multiple chips)/CDCQ item should also be entered if applicable.
b-2) The items in the row direction are based on technical aspects and CDCQ. (Add rows as necessary)
b-3) Enter the specifications for new product.
b-4) If the content is the same as the new product, write the same content as the new product instead of "○" or "←".

## Slide 8
Section c) Impact of combination
with new technology and its content:
c-1) Check the Impact of combination with new technological aspects.
c-2) If yes, enter the applicable combination.
c-1
c-2
Restricted

## Slide 9
Section d) Technical level:
d-1) Regarding the technology level,
"Existing" means the same technology and materials as experienced reference product(s).
"Minor Change" means technology and materials that are partially the same as experienced reference product(s).
Example) The individual aspects have manufacturing experience, but the combination as a whole does not. The structure has manufacturing experience, but the Grade as a whole does not.
"New technology" refers to technology and materials that have no manufacturing experience.
In the case of "Minor Change", by sharing that the risk is lower than for new technologies, it is possible to narrow the focus of the evaluation.
Additionally, test items whose test conditions are not dependent on the Grade can be omitted.
If there are extended test results that make up for the Grade difference, these should be noted in the “Additional Comment” section of the “Manufacturing Technology Assessment Sheet”.
d-2) Differences between the new technology/minor change and the existing product(s).
(including technical combinations with related processes and materials)
State the reason if not applicable
d-1
d-2
Restricted

## Slide 10
Section e) Impacts and concerns of 4M1E:
e-1
e-2
e-3
e-4
e-1) Explain why the technical level of section d) is set to "New technology" or "Minor Change” by breaking down the change point from the experienced reference product(s) in terms of 4M1E and selecting “New Technology”, “Minor Change”, or “Existing” from the pull-down menu.
For the selection criteria, refer to the " Judgement index proposal by 4M1E change point from experienced product" on the " New Point confirmation" sheet.
e-2) Describe any concerns regarding the “New Technology” or “Minor Change”.
e-3) Briefly enter the content of “New technology" or “Change Point " in terms of technological aspects (column C).
e-4) Enter the name of the existing product to be compared for each item.
Restricted

## Slide 11
■Sheet Structure
“1. Verification of New Point for Production”
The new content is linked to each new technological aspect, and for each it is used to clarify the new point(s) and level of impact from a 4M1E perspective. The basic characteristics that need to be checked in the process are extracted, and the results of this check show that there are no problems with process capability.
“2a. Verification for New Design point”
The impact of the new content on the main electrical characteristic parameters in the specifications will be clarified, and the final verification results will show that the equivalence of the electrical characteristics is maintained.
“2b. Combination Impact Confirmation & Validation Item Selection”
This section is to extract each technological aspects, which were identified by “Manufacturing Technology Assessment Sheet”, as combination aspects by breaking down into the new point aspects.
Then, identify the failure mode, qualification test items, and reason of selection for representative qualification product(s) for each and to confirm the results of the final extracted qualification test results.
■Assessment Approach
New manufacturing technology will be evaluated as OK only when process capability results in 1, the equivalency on electronic characteristics in 2a, and qualification test results selected by 2b are all OK.
1
2a
2b
Restricted
Structure of Manufacturing Technology
Assessment Sheet

## Slide 12
1. Verification of New Point for Production (1/2)
1-1
1-2
1-3
1-4
※The above is a sample from the “Front End” sheet
  1-1) Select a technical aspect (listed in section (b) with a technology level of “New Technology” or “Minor Change” in section d) of the “Manufacturing Technology Survey Sheet” from the pull-down menu.
1-2) “New and changed contents” should be copied from the section e) of the “Manufacturing Technology Survey Sheet”. If additional explanation is required, enter the comment number and enter the contents in 1-4).
1-3) Explain why the technical level of section d) is set to "New technology" or "Minor Change” by breaking down the change point from the experienced reference product(s) in terms of 4M1E and selecting “New Technology”, “Minor Change”, or “Existing” from the pull-down menu.
For the selection criteria, refer to the " Judgement index proposal by 4M1E change point from experienced product" on the " New Point confirmation" sheet.
If additional explanation is required, enter the comment number and enter the contents in 1-4).
1-4) Provide additional explanations for the comment numbers given in (1-2, 1-3). If the comment number is regarding "Minor Change" in (1-3), confirm whether the reasons for the judgment are explained.
Restricted

## Slide 13
1-5) Enter the details related to the selected “Technical Aspect”
1-6) If “New Technology” or “Minor Change” is selected in 1-3), process capability results need to be submitted as summarized evidence documents.
(Also refer to the “Example#1” Sheet”)
If the result is not yet available, write the expected completion date. If already completed, write the reference document name and page #.
1-5
1-6
Restricted
1. Verification of New Point for Production (2/2)

## Slide 14
2a-1) Write other critical parameter from the Data Sheet besides the electrical characteristics (AC, DC).
(Add as appropriate depending on the new point and new semiconductor product)
2a-2) If any specification difference occurs on the parameter, select “Yes”. If not, select “No”.
If "Yes," enter the comment number and provide additional explanation in 2a-7.
2a-3) If the new point affects the parameter, select “Yes”. If not select “No”.
2a-2
2a-3
2a-4
2a-5
2a-1
2a. Verification for New Design point
2a-6
2a-4) Select "Yes" for parameters whose electrical characteristics are to be checked using a sample. Select "No" for parameters whose electrical characteristics are not to be checked.
2a-5) If “Yes” is selected in any parameter in 2a-4), write electrical characterization results selecting by “OK” or “NG”. The actual confirmation results need to be submitted as summarized evidence documents. If the result is not yet available, provide the expected completion date.
2a-6) If “Yes” is selected in 2a-2) to 2a-4), add a comment No. in the applicable item and provide additional explanation in 2a-6).
Restricted

## Slide 15
2b-1）Manually copy the “Technical Aspect”
selected in 1-1).
2b-2) Site:
if new manufacturing site, write “X”
4M1E:
If any “Minor Change” or “New Technology” is
applicable in the section 1, write “X”.
OR: If any “X” is applicable in the above 2
items, write “X”.
2b-3） Write all possible combination risk for
each technical aspects.
2b-4）If there is production experience as an individual
aspects, but no experience as a combination
→ write about the production experience so far,
such as minor change point(s)
2b-5) Copy the concerns from the “Manufacturing
Technology Survey Sheet”
using the drop-down menu.
2b. Combination Impact Confirmation &
Validation Item Selection (1/2)
2b-8
2b-7
2b-5
2b-4
2b-3
2b-2
2b-1
2b-6
Restricted
2b-6) Enter the failure mechanism
2b-7) In case of qualification by similarity using a representative product, write the selecting condition.
2b-8) In case of qualification by similarity using a representative product, write the representative product type/part number.

## Slide 16
2b-9) Select from the following options and
input the appropriate marking for each test
in relation to the failure mechanism.
Marking Selections:
“O”：Test item
“@”：Critical test item
“-”： No test
2b-10) Referring to the ZVEI DeQuMa,
input the applicable “Type of Change” and “ID”
(Manually copy from a DeQuMa sheet)
(*DeQuMa sheet and its tutorial can be
downloaded from the ZVEI’s website)
2b-11) Manually copy the evaluation items from the ZVEI DeQuMa
sheet in relation to the ID(s) selected in 2b-10).
2b-12) The tests actually performed should be marked with an ‘O’
”O”：Actually performed
“-”：Not performed
If additional explanation is required, add a comment No.
2b-13) If the qualification has been completed,
the results need to be submitted as summarized evidence
documents. If the result is not yet available,
provide the expected completion date.
2b-14) Write additional comments with regards to
the comment No. in 2b-12).
For the key check items , conduct tests by the methods specified by ZVEI DeQuMa or “degradation sign analysis” specified by JEITA EDR-4716. For “@” (critical test item), the judgement on “degradation sign analysis” is possible based on the ECU maker's agreement and the confirmation result by the experts of Semiconductor makers.
2b-9
2b-10
2b-11
2b-12
2b-13
2b-14
Restricted
2b. Combination Impact Confirmation &
Validation Item Selection (2/2)

## Slide 17
No. | Date | Version | Note
1 | 2024/**/** | Rev_** | First Edition
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 
8 |  |  | 
9 |  |  | 
10 |  |  |