## Slide 1: Multi-Resource Differential Evaluation Sheet Tutorial

## Slide 2
Purpose of Multi-Resource Differential Evaluation Sheet
■Overview
Multi-Resource Differential Evaluation Sheet is a tool that describes the evaluation level and tests for approving part(s) with multi resources.
・ Used as a communication tool for semiconductor makers, ECU makers, and Car makers.
・This document follows the international standards (such as IATF16949, AEC Q10x, IEC 60810, and ZVEI).
The evaluation item matrix which is based on the ZVEI-Delta Qualification Matrix (DeQuMa) is to identify different point(s) and evaluation items. Based on the following contents, it will clarify the scope of evaluation required for part approval and applicable tested product(s).
・Connection between the new point(s) from 4M1E point of view and evaluation items
・Visualization of the impact on electrical components and systems by the difference(s) with the “Confirmation of design
changes due to multi-resources”
・Connection between evaluation results or production results under the manufacturing conditions with multi-resources and
evaluation items required for part approval
・Connection between combination element, actual result, failure mechanism, representative product, and evaluation items
■Purpose
  ・Optimization of evaluation item selection based on failure risk due to applying parts with multi-resources
  ・Throughput improvement, man-hour reduction for approval of parts with multi-resources by using a common form
  ・Reduction of time and effort required for approval of parts with multi-resources
Restricted

## Slide 3
Structure of Multi-Resource Differential Evaluation Sheet
■Sheet Structure
“1. Manufacturing differential check with multi-resource application”
This section is to identify the manufacturing differential(s) based on the technical aspects from 4M1E point of view and to confirm its process capability.
“2a. Differential design checks for multi-resource applications”
This section is to clarify the impact by the differential(s) from product specification point of view and to confirm the equivalency on electronic characteristics.
With the above results,
“2b. Verification of combination risk and definition of evaluation items”
This section is to identify qualification test items and reason of selection for representative qualification product(s) and to confirm the required qualification test results.
■Assessment Approach
Differential evaluation of part approval with multi-resources can be OK only when process capability results for 1, equivalency on electronic characteristics for 2, and qualification test results selected by 2b are all OK.
1
2a
2b
Restricted

## Slide 4
1. Manufacturing differential check with multi-resource application
(1/2)
1-1
1-2
1-3
1-4
1-5
1-6
1-1) Select “Reason of application” from the drop-down lists. If “Others” is selected, add a comment No. in 1-4) and write explanatory comments on 1-6).
1-2) Write production experience
1-3) Select “Multi-resource type” from the drop-down lists.
If “Others” is selected, add a comment No. in 1-4) and write explanatory comments on 1-6).
1-4) Select “multi-resource differential content” from the drop-down lists. If additional explanation is required, add a comment No. and write comments on 1-6). If there is no applicable one, leave it blank, add a comment No. , and write additional comments on 1-6).
1-5) As to multi-resource differential(s) from 4M1E point of view , select from the below 3 items
“D“ for Difference
“E” for Equivalent
“No” for No-difference
Refer to the “4M1E STD” sheet for each definition
1-6) Write additional comments for 1-1) to 1-5).
Link each comment No. to the No. added in 1-4) and/or 1-5). If “E” for Equivalent is selected in 1-5), make sure to write its justification.
Restricted

## Slide 5
1-7) If “Any correction to mitigate the differential effect in product” occurs, select “Yes”. if not, select “No”. Add comment in 1-8) if additional explanation is required by adding a comment No.
1-8) Add explanations for 1-7).
1-9) Select from the drop-down lists which link with the selected “muti-resource differential content”.
1-10) If “D” or “E” is selected in 1-5), process capability results need to be submitted as summarized evidence documents.
(Also refer to the “Example#1” Sheet”)
If the result is not yet available, write the expected completion date. If already completed, write the reference document name and page #.
1-8
1-7
1-9
1-10
1. Manufacturing differential check with multi-resource application
(2/2)
Restricted

## Slide 6
2a-2
2a-3
2a-4
2a-5
2a-1
2a-7
2a-6
2a-1) Write other critical parameter from the Data Sheet besides the electrical characteristics (AC, DC).
2a-2) If any specification difference occurs on the parameter, select “Yes”. If not, select “No”.
2a-3) If the process difference affects the parameter, select “Yes”. If not select “No”.
2a-4) If “Any correction to mitigate the differential effect in product” occurs in 1-7), select “Yes” in the applicable parameter. If not applicable, select “No”. If no correction in 1-7), “No” should be selected in all items
2a-5) If electrical characterization is confirmed using samples, select “Yes” in the applicable parameter. If not, select “No”.
2a-6) If “Yes” is selected in any parameter in 2a-5), write electrical characterization results selecting by “OK” or “NG”. The actual confirmation results need to be submitted as summarized evidence documents. If the result is not yet available, provide the expected completion date.
2a-7) If “Yes” is selected in 2a-2) to 2a-5), add a comment No. in the applicable item and provide additional explanation in 2a-7)
2a. Differential design checks for multi-resource applications
Restricted

## Slide 7
2b-1）Manually copy “multi-resource differential content”
selected in 1-4).
2b-2) Site:
if multi-site production, write “X”
4M1E:
If any “D” is applicable in the section 1, write “X”.
Correction:
If any “Yes” is applicable in the section 1, write “X”.
OR:
If any “X” is applicable in the above 3 items, write “X”.
2b-3） Write all possible combination risk for
each “multi-resource differential content”.
2b-4）If the combinations has production experience,
write “X”, if none, write “-”.
2b-5) Write failure mechanism.
2b-6) In case of qualification by similarity using
a representative product, write the selecting condition.
2b-7) In case of qualification by similarity using
a representative product,
write the representative product type/part number.
“2b. Verification of combination risk and definition of
evaluation items” (1/2)
2b-7
2b-6
2b-5
2b-4
2b-3
2b-2
2b-1
Restricted

## Slide 8
2b-8) Select from the following options and
input the appropriate marking for each test
in relation to the failure mechanism.
Marking Selections:
“O”：Test item
“@”：Critical test item
“-”： No test
2b-9) Referring to the ZVEI DeQuMa,
input the applicable “Type of Change” and “ID”
(Manually copy from a DeQuMa sheet)
(*DeQuMa sheet and its tutorial can be
downloaded from the ZVEI’s website)
2b-10) Manually copy the evaluation items from the ZVEI DeQuMa
sheet in relation to the ID(s) selected in 2b-9).
2b-11) The tests actually performed should be marked with an ‘O’
”O”：Actually performed
“-”：Not performed
If additional explanation is required, add a comment No.
2b-12) If the qualification has been completed,
the results need to be submitted
as summarized evidence documents.
If the result is not yet available,
provide the expected completion date.
2b-13) Write additional comments
with regards to the comment No. in 2b-11).
2b-8
2b-9
2b-10
2b-11
2b-12
2b-13
*Either the test method specified in ZVEI DeQuMa or “degradation sign analysis” method specified in JEITA EDR-4716 is available for the evaluation. For “@” (critical test item), the judgement on “degradation sign analysis” is possible based on the ECU maker's agreement and the confirmation result by the experts of Semiconductor makers.
“2b. Verification of combination risk and definition of
evaluation items” (2/2)
Restricted